Stranded Copper Shielding

---
Stranded Copper Testing
out of phase and scaled by α
phase shift
gain
B_{\mathrm{applied}} = B_0 \cos \omega t
B_{\mathrm{induced}} = - \alpha B_0 \sin \omega t
B = B_{\mathrm{applied}} + B_{\mathrm{induced}} = \beta B_0 \cos(\omega t + \phi)
\beta = \sqrt{1 + \alpha}
\phi = -\arctan(-\alpha)

---
\mathrm{stranded} = 1.0008 \pm 0.0005
{\mathrm{avg\;copper} \over \mathrm{avg\;stranded}} = 0.592

---
\mathrm{stranded} = 0.0375 \pm 0.0769
{\mathrm{avg\;stranded} \over \mathrm{avg\;copper}} = 0.00135

---
Stranded Copper Analysis
phase shift
gain
skin depth effect
\beta = \sqrt{1 + \alpha}
\phi = -\arctan(-\alpha)
\alpha \sim \omega
\alpha \sim \int_0^h e^{-z/\delta} \, dz = \delta - \delta e^{-h/\delta}
\delta \sim \sqrt{1 / \omega}

---
B0 Data Analysis

---
Current Procedure
- probe is offset from origin by Δr = (Δx, Δy, Δz)
- pick a field “slice,” usually the line x = 5 cm, y = 0
- compare simulated map to measured map
- transform measured map by r → r – Δr
- compare again
- keep guessing Δr until agreement is good
- problem: done per slice, not for entire field

---
Automation
- run a densely-gridded simulation and interpolate to obtain an essentially continuous map
- calculate deviation as a function of Δr
- MCMC algorithm to vary Δr until χ2 is minimized
- moving measured map around in 3D until it fits
\chi^2 = \sum_{\mathrm{points}} { |\vec{B}(\vec{r} - \Delta\vec{r}) - \hat{\vec B}(\vec r)|^2 \over |\boldsymbol\sigma|^2}