Copper Strand Thermal Shielding
for Third-Scale Magnet
Aritra Biswas
July 13, 2015

---
Third-Scale Magnet
- superconducting lead
  (Tc = 7.2 K) for B field uniformity
- thermally-shielded warm bore to map B field
- copper plating on G-10 for insulation
- can't interfere with B field
thermal shield cover
warm bore

---
Our Thermal Shield
- strands of copper held together by epoxy
- currents can't jump between insulated strands
- no large-scale eddy currents
- measure B field interference and compare with copper plate

---
setup inside B0 coil driven by AC
alternating field in x direction
z
x
central axis
gain:
phase shift:
B_x
probe
B_x = B_0 \cos(\omega t + \psi)
B_x
probe
B_x' = B_0' \cos(\omega t + \psi')
\gamma \equiv {B_0' \over B_0}
\Delta\psi \equiv \psi' - \psi

---
\mathrm{sensitivity} \approx { \textcolor{blue}{\mathrm{blue\;rectangle}} \over \textcolor{red}{\mathrm{red\;rectangle}} } = 0.454 \pm 0. 0001

---
\mathrm{sensitivity} \approx { \textcolor{red}{\mathrm{red\;rectangle}} \over \textcolor{blue}{\mathrm{blue\;rectangle}} } = 1.6 \times 10^{-3} \pm 1.2 \times 10^{-5}

---
Predicting γ(ω) and Δψ(ω)
skin depth shielding
induction on plane
x
x
B_{x,\mathrm{applied}} = B_0 \cos(\omega t + \psi)
\beta B_0 \cos(\omega t + \psi)
\alpha B_0 \sin(\omega t + \psi)
\gamma = \sqrt{\alpha^2 + \beta^2}
\Delta\psi = -\arctan(-\alpha/\beta)
B_{x,\mathrm{final}} = \gamma B_0 \cos(\omega t + \psi + \Delta\psi)
e^{-x/\delta}
-\pd{\Phi}{t}

---
Remarks
- phase shift sensitivity in 400-800 Hz range:
- shielding parameters:
1.6 \times 10^{-3} \pm 1.2 \times 10^{-5}
\beta \sim {1 + e^{-c/\delta} \over 2}
\delta = \sqrt{2 \rho \over \omega \mu_r \mu_0}
\alpha \sim \omega e^{-c/2\delta} \sinh\left(c \over \delta\right)